## Slide 1: Business Considerations
In this section you learn how to:
Identify some key business considerations before setting up work centers, routings, and WO subcontracting in QAD Enterprise Applications
Set up departments, work centers, comments, standard operations, routings, and processes in QAD Enterprise Applications
Process subcontract operations in QAD Enterprise Applications

## Slide 2: Business Issues
Repetitive
Shop Floor Control
Subcontracting
Capacity Requirements Planning
Burden/Labor Rates

## Slide 3: Repetitive and Shop Floor Control
The repetitive and shop floor control modules in QAD Enterprise Applications require routing operations
DAILY PRODUCTION
Notes: At setup:
create prefixes, to make all requisition and PO number unique across the network.
Create address codes to match the site codes; otherwise the system does not know where to send the orders

## Slide 4: Repetitive and Shop Floor Control
When may routing operations not be required?
When control of manufacturing processes and related costs and capacities is not required or desired
When item lead times are very short
If the total item cost is mostly material and overhead and the labor component is low
If capacity is easily managed
When the repetitive module is not in use
The repetitive and shop floor control modules in QAD Enterprise Applications require routing operations
Notes: At setup:
create prefixes, to make all requisition and PO number unique across the network.
Create address codes to match the site codes; otherwise the system does not know where to send the orders

## Slide 5: Subcontracting
Receiving
Purchasing
Western Tumble
Deburr Incorporated
Operation 2
Your Company
Operation 1
Operation 3
Notes: At setup:
create prefixes, to make all requisition and PO number unique across the network.
Create address codes to match the site codes; otherwise the system does not know where to send the orders

## Slide 6: Subcontracting
Your Company
Western Tumble
Deburr Incorporated
Operation 2
Operation 1
Operation 3
Set up at least one department for outside work.
Set up at least one work center for each type of subcontract operation.
Set up subcontracting operations in routings.
Notes: At setup:
create prefixes, to make all requisition and PO number unique across the network.
Create address codes to match the site codes; otherwise the system does not know where to send the orders

## Slide 7: Capacity Requirements Planning (CRP)
Work centers are the basic unit for CRP
Work center capacity equals
calendar hours available x number of machines
Notes: At setup:
create prefixes, to make all requisition and PO number unique across the network.
Create address codes to match the site codes; otherwise the system does not know where to send the orders

## Slide 8: Burden/Labor Rates
Burden costs use
Machine burden rate
Labor burden rate
Labor burden %
Labor rates
The system uses these elements in calculating item costs
Notes:     Memo items are expensed or capitalized on receipt, depending on the purchases account for the line items. Memo items do not update inventory.
Non-inventory (memo) items are those items not listed in the item master.
Memo items have no effect on MRP and do not update inventory.
You can obtain inventory items through a memo purchase, for example, for as-needed production materials and inventory for non-production departments.
You can cost or expense these items in the PO Control File (5.24). Memo items are expensed or capitalized on receipt, depending on the purchases account for the line items.

## Slide 9: Burden/Labor Rates
Burden costs use
Machine burden rate
Labor burden rate
Labor burden %
Machine burden rate equals
(standard setup hours x number of machines + standard run hours) x work center machine burden rate
Notes:     Memo items are expensed or capitalized on receipt, depending on the purchases account for the line items. Memo items do not update inventory.
Non-inventory (memo) items are those items not listed in the item master.
Memo items have no effect on MRP and do not update inventory.
You can obtain inventory items through a memo purchase, for example, for as-needed production materials and inventory for non-production departments.
You can cost or expense these items in the PO Control File (5.24). Memo items are expensed or capitalized on receipt, depending on the purchases account for the line items.

## Slide 10: Burden/Labor Rates
Burden costs use
Machine burden rate
Labor burden rate
Labor burden %
Labor burden rate equals
(standard setup hours/order quantity + standard run hours) x work center labor burden rate
Notes:     Memo items are expensed or capitalized on receipt, depending on the purchases account for the line items. Memo items do not update inventory.
Non-inventory (memo) items are those items not listed in the item master.
Memo items have no effect on MRP and do not update inventory.
You can obtain inventory items through a memo purchase, for example, for as-needed production materials and inventory for non-production departments.
You can cost or expense these items in the PO Control File (5.24). Memo items are expensed or capitalized on receipt, depending on the purchases account for the line items.

## Slide 11: Burden/Labor Rates
Burden costs use
Machine burden rate
Labor burden rate
Labor burden %
Labor burden percent equals
(standard setup hours x work center setup rate x labor burden %)
+
(standard run hours x work center labor rate x labor burden %)
Notes:     Memo items are expensed or capitalized on receipt, depending on the purchases account for the line items. Memo items do not update inventory.
Non-inventory (memo) items are those items not listed in the item master.
Memo items have no effect on MRP and do not update inventory.
You can obtain inventory items through a memo purchase, for example, for as-needed production materials and inventory for non-production departments.
You can cost or expense these items in the PO Control File (5.24). Memo items are expensed or capitalized on receipt, depending on the purchases account for the line items.

## Slide 12: Course Overview
Introduction to work centers and routings
Business considerations
Set up departments, work centers, comments, standard operations, routings, and processes in QAD Enterprise Applications
Process subcontract operations in QAD Enterprise Applications